## Slide 1
Impedance and Collective Effects
Bocheng Jiang
（姜伯承）
jiangbocheng@cqu.edu.cn
2025/08/01

## Slide 2: Contents
Introduction to Collective effects
Wakefield & impedance
Space charge effect
Coupled bunch instability
Ion instability
Single bunch instability
Beam-beam effect
IBS effects & Touschek lifetime
Damping
Summary

## Slide 3
Introduction to Collective effects

## Slide 4
Introduction to Collective effects
The motion of particles is highly ordered.
The motion of particles is （mainly）determined by external electromagnetic fields.
Particles in an accelerator ~ 101~14
The self field may play role when particle number is high (Collective effects)
The time of the stable motion can be ꝏ
Energy up to 10TeV
VS
Tokamak
Developed
Developing
Accelerator
The motion of particles is in random.
The motion of particles is majorly determined by self fields.
Particles in a Tokamak ~ 1019~20 （10-3mol）
The time of the stable motion around 1000s at present
Energy ~10keV non-relativistic

## Slide 5
Introduction to Collective effects
Once upon a time accelerator physics want to develop a fusion device based on accelerator.
To achieve enough nuclear reaction the large amounts of particles(1014）should be transversely focused to bellow 1μm. For such a low energy beam, space charge effects will be a big challenge for focusing.
We will introduce space charge effects as one of major collective effects for low energy beam later
The maximu cross section D-T fusion @110 keV is

## Slide 6
Introduction to Collective effects
How far have we gone
Synchrotron
KEK B factory
2.6 A @3.5GeV (average beam current)
Induction linac
ATA LLNL
10kA @50MeV （peak current）
60ns pulse
Plasma wake-field accelerator
20–40 kA (peak current)
~30fs
Tokamak ~ million Amp

## Slide 7
Introduction to Collective effects
The behavior of Charged particles interact with magnets, RF field is usually called single particle beam dynamics.
Wakefield interaction
Ions or electron clouds
Particles collision
Space charge force
Coherent synchrotron radiation
Above-mentioned effects can be categorized to collective effects. They depend on charge density, peak current or average current.
Results：Beam performance degraded，charge reduction or even beam loss 。
Landau damping
RMS size
Centroid

## Slide 8
Single particle beam dynamics is well established. One of the most important method is factorization.
Introduction to Collective effects
Accelerator design is only to work on M （lattice design), which significantly simplifies the problem. For any initial condition , there's no need to repeat the entire analysis—as long as the system remains in the linear regime.
For comparing, once we enter the nonlinear regime, the problem becomes much more complex. For example, studying the beam Dynamic Aperture requires extensive numerical computation.
There is no universal solution to collective effects.
They should be addressed individually by various methods.

## Slide 9
negative mass instability 1959
resistive wall instability 1960
Robinson instability 1964
beam breakup instability 1966
head-tail instability 1969
microwave instability 1969
Landau damping 1969
beam-beam limit in colliders 1971
potential well distortion 1971
Sacherer formalism 1972
anomalous bunch lengthening 1974
transverse mode coupling instability 1980
hose instability 1987
coherent synchrotron radiation instability 1990
sawtooth instability 1993
electron beam-ion instability 1996
electron cloud instability 1997
microbunching instability 2005
interplay of multiple instability mechanisms 2013
Over the years, accelerator physicists have observed, explained, and (mostly) cured several intricate instability mechanisms. An incomplete list follows below
Alexander Wu Chao, Lectures on Accelerator physics, World Scientific, 1st edition, 2020, ISBN 9789811227967.
Introduction to Collective effects

## Slide 10
Instability
Coherent instability
Incoherent instability
Particles in a bunch oscillate coherently, can be treated as macro-particle.
Particles move incoherently
Oscillate Amplitude increased
Bunch distorted, beam size increased, beam energy increased.
beam lifetime
Particles loss when exceeding acceptance (Transverse acceptance or Momentum acceptance)
Beam current decay gradually
Introduction to Collective effects

## Slide 11
Wakefield & impedance

## Slide 12
Wakefield & impedance
z
When a charge beam passing through a beam pipe which gets discontinuities or gets finite conductivity. The EM field will be excited, it is called wakefield.
Wakefield decay with time, it will disturb the motion of tail particles or the following bunches.
The wakefield is the main sources of beam instaiblity

## Slide 13
Wakefield & impedance
Wakefield can be expressed by the wake function。It an integral value.
Wake function is a Green function, where independent variable “z” denotes distance of witness beam following the source beam.
Wake function is a characterizes of vacuum chamber not the beam. Wakefield = Wake function convolution source charge distribution
Wake function
Wakefield (wake potential)
z

## Slide 14
Wakefield & impedance
Conservation of Energy
Panofsky-Wenzel Theory
Causality
Beam loading
Wake function properties

## Slide 15
Wakefield & impedance
Panofsky-Wenzel Theory
For a axial symmetry structure, we can get Panofsky-Wenzel Theory of wake field.

## Slide 16
Wakefield ----》Tracking。
Impedance ----》Analysis。
Time domain
Frequency domain
Im Im
Simulation codes：CST Microwave Studio, GdfidL, ABCI, Mafia,
Wakefield & impedance
Impedance is the Fourier transform of the wake function.
Panofsky-Wenzel Theory for impedance

## Slide 17
Wakefield & impedance
Narrow-band impedance： High Q cavity like structure, long range wakefield, resonance peak. Important for multi bunch instability.
Resonance model
Broad-band impedance: Low Q structure, short range wakefield, spectrum is broad. Important for single bunch instability.
Effective broad-band impedance
Resonance frequency

## Slide 18
Wakefield & impedance
Parasitic energy loss
When a beam passing through a beam pipe, a wakefield is generated, beam energy will loss due to impedance.
Where is the loss factor, q is bunch charge.
Unlike impedance, the loss factor depends on the bunch length—the shorter the bunch, the higher the loss factor. The associated energy loss will deposit onto the beam pipe, causing it to heat up. The energy loss increases quadratically with the bunch charge it should be seriously considered for high charge bunch.

## Slide 19
Space charge effect

## Slide 20
Space charge effect
The space charge force describes the interaction between particles their distance is greater than the Debye length.
T is “Temperature” of the bunch，n0 particle density in the bunch
Debye length
If particles distance is smaller than the Debye length, the interaction is described by Scattering.
e-
e-
e-
P+
The Lorentz force ：
R
line
For r<R
Coulomb's law of line charge

## Slide 21
Space charge effect
When two same type particles move in same direction, the electric field force repulse each other, the magnetic force attract each other.
When beam is ultra relative （）, electric and magnetic forces will cancel each other, thus space charge force is seriously considered when beam is at low energy.

## Slide 22
Fx
Fx
x
y
y
x
x
x
3σ
Uniform distribution
Gaussian distribution
For a Gaussian distribution, the force is highly nonlinear.
Bassetti-Erskine given the space charge force for the first order approximation:
For a transverse uniformly distributed beam，The space charge force is linearly increased with radius inside the beam, it is very similar to a defocusing force.
eλ where is line charge density in longitudinal coordinate, σx,y is transverse RMS bunch size.
Space charge effect
The space charge force is inverse proportional to σ2x,y and , and proportional to, the space charge force will be very large when beam size is very small, beam energy is very low and charge line density is large.

## Slide 23
Tune shift can be estimated by the defocus force：
The normalized emittance growth when the beam passing through a drift L is：
I is bunch peak current，s is longitudinal coordinate，L drift length，G is geometric factor，b is pipe radius.
A more accurate method is using simulation code such as PARMELA to evaluate space charge effect.
Space charge effect
The space charge force will cause tune shift, emittance growth.

## Slide 24
Coupled bunch instability

## Slide 25
Coupled bunch instability
If wakefield decay slowly, the wakefield will interact with following bunches or even bunches in following turns，This interaction will cause coupled bunch instability.
The slowly decayed wakefield is named long range wakefield which hold high quality factor Q
The impedance is narrow banded.
Narrow band impedance is produced by cavity like structure or resistive wall.

## Slide 26
Where ωβ is betatron oscillate frequency，n denotes the bunch index to be investigated, m denotes bunch excite wakefield. M is the harmonic number of the ring, C is the circumference of the ring，γ is relative energy，T0 is revolution period, N is number of electrons in a bunch, a is shaping factor.
Transverse coupled bunch instability
，
Assume bunch oscillation gets form:
(1)
(2)
Substituting Eq.(2) into Eq.(1)，With Fourier transform we get:
(3)
Coupled bunch instability

## Slide 27
If there are M bunches evenly filled in the ring, the motion can be separated into M modes，the μth mode get following form：
, μ=( 0,1,2…M-1)
(4)
tune shift，imaginary part will be the growth rate.
(5)
Substituting Eq.(4) into Eq.(3)，we get:
Coupled bunch instability
(3)
Rewrite (3),
It can be simplified by mode separation

## Slide 28
Take resistive wall impedance as an example, where is the conductivity of the metal.
(6)
If sum of real part of impedance in Eq.(6) <0，it will cause instability. Where =νβω0, it can be deduced that fraction part of νβ <0.5 will benefit resistive wall instability.
μ ω0 –ωβ μ= - floor(νβ)-1
(μ +M)ω0 -ωβ
Coupled bunch instability
If ，only k=μ terms left in Eq.(5), all the other terms equals 0. Eq.(5) can be further simplified:

## Slide 29
Longitudinal coupled bunch instability can be done in a similar way:
Where is slip factor, , Real part of the impedance will contribute to instability. Re an even function，first part in sum is 0 (for uniformly filled ring) . Only second term with sideband contribute to instability.
Narrow band longitudinal impedance is mainly from HOM of RF cavity. It becomes dangerous when fHOM close to . When number of HOMs is limited, the cavity can be detuned to avoid instability. However, when there are large number of HOMs, it is difficult to do so, the only way is to damp HOM to reduce the impedance.。
(7)
The resonance frequency of RF cavity accl mode ωrf ≈M in order built up enough RF voltages feed by RF power. To efficiency build up RF voltage, the impedance of the accl mode should be large. The accl mode will be dangerous, the instability is called Robison instability, the criterion can be expressed:
Robinson instability for >0
Coupled bunch instability
The only way to avoid Robinson instability is to detune the cavity.

## Slide 30
Coupled bunch instability
For some cases, when cavity Q is not so high and ring circumference is large, the spectrum width is comparable to revolution frequency. The -1 mode frequency can still overlap with impedance, may cause -1 mode instability.
Then arrive at a conclusion that larger ring will be more sensitive to the longitudinal coupled bunch instability.

## Slide 31
Ion instability

## Slide 32
Ion instability
Ion production：Residual gas molecules can be ionized by the beam collision or by the synchrotron radiation photodecomposition.
The ionized electrons will be expelled away form closed orbit and get no effects on beam.
Electron bunch
Ion
Ion trap
Fast ion
Ion instability
Ion trap Ions accumulate in multi turns.
fast ion instability Ions accumulate along bunch train, drift away after train.

## Slide 33
Ion trap
When an electron bunch passes through, the ions will experience an attractive force proportional to their transverse distance from the beam center. Therefore, it can be treated as a focusing lens.
Where A is molecular mass number， classical radius of the proton， electron number in the bunch， transverse electron beam RMS beam sizes. If electron bunch is uniformly filled in the ring, the ion will receive a periodic focus which can be represented by transfer matrices:
If ion motion is stable, it will be trapped around closed orbit. For the stable motion, the absolute value of the trace of the matrix <2, gives out Eq.(8)
Which means the molecular mass number greater than Eq.(8) will be trapped. As more and more ions are trapped, the beam will be unstable. However, the molecular in pipe is mainly H2 (A=2), CO/N2 (A=28), Ar (A=40), CO2 (A=44) , they are easily escaped.
Ion instability
(8)

## Slide 34
From Eq.(8) it can be found, lower the transverse beam size, larger the beam current will prevent ion trapping.
Lower the vacuum pressure will reduce ion trapping numbers.
Besides above solutions, there is another method to prevent ion trapping: Non-uniform filling
Non-uniform filling will break the periodic focus lattice, making ion motion unstable. A common filling pattern is a bunch train followed by empty buckets(ion clearing gap) letting ion drift away during the gap.
500 bunches
220 empty buckets
One of the filling patterns in SSRF storage ring.
Ion instability
Ion trap

## Slide 35
Fast ion instability
is density of residual gas molecular, cross section of ionization，nb bunches number in the bunch train，Lsep is the bunch separation in the train.
Ion instability can develop even when there is an ion clearing gap if the vacuum pressure is not sufficiently low. The ions produced by the bunches in the front of the train will affect the motion of the tail bunches. This phenomenon is known as fast ion instability, and its growth rate can be expressed as follows:
The fast ion instability in SSRF storage ring, the oscillation amplitude increased along the bunch train， When collimator closed, the tail bunches loss charge.
Multi bunch train filling to suppress fast ion instability.
Ion instability
500 bunches
220 empty buckets

## Slide 36
Single bunch instability

## Slide 37
Single bunch instability
a、Beam Breakup （BBU）
Usually happens in linac, where particles in head and tail of the bunch do not exchange.
When bunch charge is high, wakefield is great.
The launch beam is off-axis.
The particles at the tail of the bunch feel the wake generated by the particles at the head. This causes the transverse oscillation amplitude of the tail to increase, deforming the bunch into a banana shape and eventually leading to beam breakup.

## Slide 38
a、Beam Breakup （BBU）
Two particle model：Head particle #1，tail particle #2，separation distance z，The equation of motion of #2:
w is the wave-number of β oscillation in linac，L is the length of accelerator cavity, is the transverse wake function of an accelerator cavity，oscillation amplitude of head particle. The motion of #2 can be written:
The first term in right hand of Eq.(9) is a free betatron oscillation. The second term is relative to wakefield. After accelerate length L0，the amplitude increased by a factor：
Eq. (10) without considering energy increment. When energy increment (-> ) is considered, the adiabatic damping will play role:
Single bunch instability
(9)
(10)

## Slide 39
a、Beam Breakup （BBU）
When BBU should be seriously treated？ When acceleration structure is small such as X band accelerator, dielectric wakefield accelerator who pursue high gradient acceleration（）.
How to fight against BBU
  Stronger focus，increasing
  More efficient acceleration, better adiabatic damping.
  Better alignment, the injection beam is closer to center.
  Add the BNS damping mechanism (Balakin-Novokhatsky-Smirnov)
  Slab-symmetric structure + flat beam(for dielectric wakefield)
BNS damping: let head particle a tune shift with tail particle.
Single bunch instability
a
  slab-symmetric structure + flat beam
metal
Dielectic
x
y
z
  σx>>a;σx>> σy
  becomes uniform, Panofsky-Wenzel Theory, greatly suppressed

## Slide 40
b、Head tail instability
Unlike in a linac, bunch in a storage ring will exchange it particles between head and tail caused by synchrotron oscillation.
Synchrotron oscillation will cause energy variation, when chromaticity ≠0, the betatron tune will be variated.
Two particle model
C is ring circumference, is chromaticity, is synchrotron oscillation angular frequency.
Single bunch instability

## Slide 41
Single bunch instability
b、Head tail instability
The transfer matrix for a whole synch period
The growth rate can be found
W时，“+” mode is stable, while “-” mode is unstable. Solving the Vlasov equation can get more accurate solutions，which shows we have overestimated the growth rate of “-” mode by the simplified model which can be damped by synchrotron radiation and Landau damping. For ring>0，we can choose working point 0.
The eigenvalue of the matrix is

## Slide 42
c、Transverse mode coupling instability (TMCI）
Though head tail instability can be avoided when 0，when bunch current further increased, another instability TMCI will occur. Transverse mode 0 and -1 mode frequency will be shifted, when their frequency merged, turbulence will happen, which will cause instability, the threshold can be written:
UTEF ring TMCI simulation result
is average radius of the ring， longitudinal broad band impedance, , is revolution frequency.
Single bunch instability

## Slide 43
d、CSR instability
Incoherent radiation
Coherent radiation
When the radiation wavelength is close to or longer than the bunch length, coherent synchrotron radiation (CSR) will be emitted. In a dipole, electrons move on a curved path, and the CSR will catch up with the leading electrons. As the electrons get transverse momentum, they will interact with the CSR.
In a storage ring where η≠0 (R56 ≠0), energy modulation will cause density modulation, creating micro-bunches. These micro-bunches will enhance CSR, leading to an instability. This process is very similar to FEL, except with a longer wavelength and in an uncontrolled way.
If above process happens at the place where gets dispersion, transverse emittance will be increased.
CSR can be shield by vacuum chamber.
Single bunch instability
wakefield
CSR
Why?

## Slide 44
P’
P
P’
P
A
B
C
P’
P
P’
P
D
CSR can also be investigated by “wakefield” &“impedance”，Unlike EM field, it effect leading particles.
3D model can describe CSR more accurate, it is complex. We usually using1D model, 1D model will somewhat overestimate the problem.
P’ is the macro-particle emit CSR，P is the macro-particle effected by CSR，There are four cases A, B, C, D as shown in left，Among which B is most important，We take B for example to calculate CSR wake function，it is shown in Eq.(11)，where R bending radius，z is distance between P’ and P.
μ
CSR wake is the convolution wake function with bunch charge density.
(11)
(12)
It can be found in Eq.(11) is a monotonically increasing function which is far from EM field. Eq.(12) gets singularity, needs P.V. integration.
Single bunch instability
d、CSR instability

## Slide 45
For EM wake, it is Cos like or combination of Cos waves，Specified longitudinal distributions can be found to make the wakefield flattened (covering most part of the bunch) which will benefit the instability.
However, for CSR wake, it is pointless to find a situation like left side. It means CSR will inevitably increase the energy spread.
charge
Wakefield
How to suppress CSR instability？
In a linac, suppress CSR effect usually refers to control the transverse emittance growth.
In a storage ring suppress CSR instability is to control the development of micro-bunch.
d、CSR instability
Single bunch instability

## Slide 46
In a linac, such as driving for an FEL, the peak current is very high, CSR is a serious problem. Any bending should be carefully treated. Chicane is used to suppress the bunch length, where CSR will degrade the beam performance.
The energy modulated by CSR is different to the energy spread heated by ISR. ISR is a random process, the energy spread increment mapping to transverse plane causing an emittance growth is inevitable unless dispersion is free. However, energy modulation caused by CSR is predictable, by a wise Lattice design the emittance growth can be cancelled between dipoles.
Single bunch instability
d、CSR instability

## Slide 47
CSR instability threshold in a storage ring can be written（Stupakov & Bane) ：
Where is initial bunch length， is energy spread， is bending radius， is Alfven current=17.045kA。
Increase energy spread is powerful method to suppress CSR instability.
Most of the ring present CSR bursts as CSR instability happens.
Single bunch instability
d、CSR instability

## Slide 48
Stable CSR
Few machine can provide stable CSR such as BESSY II, there are 1～2 weeks annually operating in low alpha mode, to create high flux THz radiations.
Single bunch instability
d、CSR instability

## Slide 49
e、Microwave instability
The instability caused by the short range longitudinal EM wakefield is called Microwave instability.（Some literature also call CSR instability to Microwave instability）.
Microwave instability and CSR instability is very similar，but still some differences：
Microwave instability | CSR instability
Tail particles are affected | Leading particles are affected
Wakefield all around ring | CSR wake appear in Bend
Wakefield proportional to Q | Wakefield proportional to Q2
The instability criterion can be gotten by solving Vlasov equation on bunch longitudinal distribution ：
However the mathematics is difficult.
Single bunch instability

## Slide 50
e、Microwave instability
Single bunch instability
Keil-Schnell-Boussard criterion is given here:
is effective longitudinal broad band impedance.
m usually to be 1.
Steady energy spread growth is more likely to be observed
Sometimes it is called SPEAR 1/3 low.
Microwave burst in SLC damping rings (9.9GHz)

## Slide 51
Beam-Beam effects

## Slide 52
Beam-Beam effects
Beam-beam effect is a particular phenomenon in colliders when beams get collision.
When beams moves collinearly in the same direction, the space charge force vanishes.
When beam moves in opposite direction, electric and magnetic force added up, providing additional focusing force（for different charged beams）.

## Slide 53
Beam-Beam effects
The transverse kick of round beam head on collision can be expressed:
Where Δt is the interaction time of two bunches
For flat beam, beam-beam parameters can be defined
For round beam, beam-beam parameters can be defined
Linear part
Nonlinear part
The effect of Nonlinear part needs tracking.

## Slide 54
For small and Q (transverse tune) not too close to 0.0 and 0.5, Tune shift caused by beam-beam effect:
Beam-beam effect distorts the linear optics, drive even order resonance; as the tune shift increases, the luminosity gain becomes less efficient with increasing beam current.
One way to reduce the beam-beam effect is to collide beams with large Piwinski angle.
A large Piwinski angle may reduce luminosity; however, the weakened beam-beam effect allows for an even smaller 𝛽y*, which can significantly enhance luminosity.
Beam-Beam effects

## Slide 55
IBS effects & Touschek lifetime

## Slide 56
IBS effects & Touschek lifetime
When distance between particles is shorter than Debye length，the interaction should be treated as scattering, Intra beam scattering (IBS) and Touschek effect play roles.
A small angle scattering will cause a small fraction of momentum exchange, it will increase the energy spread，as the scattering take place where the dispersion nonzero, the scattering will increase transverse emittance. It is call intra beam scattering.
It is very similar to incoherent synchrotron radiation (ISR): IBS is a scattering between electrons, ISR can be considered as electrons scatted by photons (magnetic field).
IBS – ISR also get difference
IBS takes place all around the ring, ISR takes place only where exists ‘photons’ (bending magnets, undulator, wiggler, or a real laser Compton scattering). It is more complex to optimize emittance growth caused by IBS because H function should be optimized all around the ring. While for ISR, only H function at bending magnet should be considered.
IBS probability of occurrence changes all around the ring according to Twiss parameters (beam size), ISR is fixed as long as bending magnet is fixed.
The natural emittance caused by ISR is the balance between quantum excitation and radiation damping. IBS will not create damping, as energy spread, emittance growth, beam size increased which alleviate IBS, the balance is more complexed.

## Slide 57
IBS causing emittance and energy spread growth can be calculated by Piwinski formula
IBS effects & Touschek lifetime

## Slide 58
When two electrons scatter with a large amount of momentum exchange, both will exceed the momentum acceptance of the ring and get lost. The beam current will decay due to particle loss. This process is called the Touschek lifetime.
For a Gaussian beam, at ultra relative energy , the Touschek lifetime can be calculated as follows:
Where is electrons in a bunch, is momentum acceptance of the ring.
Touschek lifetime is proportional to ~cubic(^2.**) of momentum acceptance and cubic of beam energy. For low energy ring Touschek lifetime is a dominant lifetime.
Increasing the momentum acceptance and stretching bunch length is the way to increase Touschek lifetime.
IBS effects & Touschek lifetime
C(ε)
ε

## Slide 59
Beam lifetime
There are various mechanisms that cause gradual electron loss, leading to an exponential decay of the beam current. This phenomenon is described by the term 'beam lifetime'
Where τ is the beam lifetime. This 'lifetime' differs from the lifetime of a single particle; it is a concept of collective effect. It describes how long a bunch composed of a large number of electrons will exist in the ring.
Quantum lifetime
For an electron storage ring, due to quantum excitation, electrons have a Gaussian distribution in 6-D phase space. In engineering, it is generally considered that the density beyond 3σ is close to zero, but it is not strictly zero. In physical analysis, this cannot be ignored. If there is a blocker at 3σ as shown in the left figure (indicated by the blue vertical line), particles greater than 3σ will be lost, meaning the Gaussian distribution (purple curve) is truncated. However, due to quantum excitation, electrons will re-balance to a new Gaussian distribution curve (indicated by the red dashed line), meaning some electrons will migrate beyond 3σ space. These outward-migrating electrons will continue to be lost when they encounter the blocker. The continuous loss of electrons leads to beam quantum lifetime
Where i can be x,y,s，is damping time， is beam size， is the acceptance (aperture).
changes drastically with the aperture , quantum lifetime will be hours

## Slide 60
Beam lifetime
Quantum lifetime
Aperture X/σx | 4 | 5 | 6 | 7
τq | 3.7s | 215s | 10.1 h | 4952h
For a storage ring with damping time τ=20ms, the quantum lifetime caused by horizontal aperture is as shown bellow
A rough estimation: Aperture X = 2σx
The fraction of particles whose amplitudes exceed 2 sigma, is 4.5%。To decay to 1/e charge, should lost 63.21% of initial charge. 63.21/4.5≈14
14*20ms=280ms

## Slide 61
The presence of residual molecules in the vacuum pipe can cause electrons to be scattered by these molecules and subsequently lost. This phenomenon is known as gas scattering lifetime.
The Coulomb scattering of electrons on the residual gas nuclei can cause the transverse oscillation amplitude of the electrons to increase beyond the transverse acceptance, resulting in particle loss. This beam lifetime, known as gas elastic scattering lifetime, can be calculated using the following formula: ：
W is gas density，Z is atomic number of the gass， is averaged beta function， is transverse acceptance.
Electrons also interact with the residual gas nuclei, undergoing bremsstrahlung. When the energy of the scattered electrons exceeds the energy acceptance, the particles are lost. This process is referred to as the gas inelastic scattering lifetime:
The overall beam lifetime can be calculated:
Beam lifetime

## Slide 62
Damping

## Slide 63
Damping
1、 Adiabatic damping：
(1)
Consider a transverse motion when beam is accelerated
（2）
The amplitude of is constant,
(3)
Replace y with
In a linac, the geometry emittance will be reduced when beam is accelerated, , which is not convenient to describe beam performance, usually normalized emittance is used in a linac

## Slide 64
Damping
The radiation direction is parallel with electron trajectory. which takes away transverse momentums, however the energy compensated by RF cavity is absolute longitudinal. This will bring damping mechanism.
2、Radiation damping：

## Slide 65
2、Radiation damping：
Damping
The damping effect in the longitudinal plane arises from the properties of synchrotron radiation: particles with higher energy lose more energy, while those with lower energy lose less. This results in D > 0.
Synchrotron radiation
For first order expansion
The longitudinal motion
It is a damped oscillation equation, the solution is

## Slide 66
3. Landau damping：
Damping
Landau damping, named after its discoverer, Soviet physicist Lev Davidovich Landau (1908–68), is the effect of damping (exponential decrease as a function of time) of longitudinal space charge waves in plasma or a similar environment.
In Wave–particle interactions
In the wave's frame of reference. Particles near the phase velocity become trapped and are forced to move with the wavefronts, at the phase velocity. Any such particles that were initially below the phase velocity have thus been accelerated, while any particles that were initially above the phase velocity have been decelerated. Because, for a Maxwellian plasma, there are initially more particles below the phase velocity than above it, the plasma has net gained energy, and the wave has therefore lost energy.
This provide a damping mechanism of the wave passing through the plasma.

## Slide 67
3. Landau damping：
Damping
Wake field – beam interaction
We borrow this concept for accelerators: when a wakefield interacts with a beam, only particles whose oscillation frequency is close to the wakefield frequency can effectively interact with it. If a particle's oscillation frequency is far from the wakefield frequency, the energy exchange is and will soon resulting in backflow.
A fraction of the beam absorbs the wakefield while the beam as a whole will remain stable. Unlike the previous case, the energy of the wakefield originates from the beam itself. This means that the energy used to excite the wakefield by the entire beam will be absorbed by a fraction of the particles, effectively creating a damping mechanism."
Absorb energy
Backflow energy
Small frequency difference
Large Frequency difference

## Slide 68
]
=
3. Landau damping：
With tune shift (real and imaginary) caused by impedance, substitute them into Eq.(13) there will be a stable regime which is larger than that without Landau damping.
(13)
Damping
In practical, the tune spread provide damping rate
=
Where is the tune spread of Half-width-at-half-height

## Slide 69
Larger the tune spread, stronger the Landau damping.
3. Landau damping：
Transverse tune spread:
Longitudinal tune spread: High harmonic cavity（Landau cavity）
Octupoles (Amplitude dependent tune shift, should compromise with DA optimization).
AC quadrupole/RF quadrupole.
Linear focus
Nonlinear focus
Damping

## Slide 70
Damping
Electron cooling for proton or ion beams is so successful, that …
e-
Besides synchrotron radiation, is there any other mechanism to cool electron beam?
PHYSICAL REV I EW LETTERS, 1998, Zhirong Huang and Ronald D. Ruth
Electron cooling for proton or ion beams

## Slide 71
Some other damping mechanism
Feedback system
Stochastic cooling
Damping
J. Jarvis et al., Nature | Vol 608 | 11 August 2022 | 287
Transverse cooling is achieved by sensing the particle displacements in the pickup and applying a correcting signal at the kicker. Normally, the pickup and kicker are placed 90◦ apart in betatron phase so that a position displacement at the pickup will become an angular displacement at the kicker.
Longitudinal and transverse feedback are engineering techniques rather than physics, yet they play a crucial role in combating beam instabilities.
Longitudinal oscillations are relatively slow, so only a single BPM (pickup) is needed to calculate the required kick.
Transverse feedback was traditionally implemented as a mode-by-mode system. With advances in electronics, bunch-by-bunch feedback is now feasible. This allows the entire feedback process to be completed within one turn. As a result, two BPMs are required to determine the necessary kick — both its amplitude and phase.

## Slide 72
Summary
Coupled bunch instability: The spectrum of the impedance and the beam overlap? If YES , which side bands feels larger impedance?
Single bunch instability: Beam evolution in phase space. Head-tail prevents instability growth, Otherwise BBU will be very powerful.
Scattering: Cross section? Acceptance?
Damping: The unsung hero, should not be neglected , the gifts of the Mather Nature.
To the end, we are so proud that most of the collective effects have been solved or understood.

## Slide 73
Reference
Alexander Wu Chao, Physics of Collective Beam Instabilities in High Energy Accelerators, John Willey & Sons, 1993.
Andy Wolski, Damping Ring Design and Physics Issues, 4th International Accelerator School for Linear Colliders Beijing, September 2009.
蔡承颖(Cheng-Ying Tsai), 电磁辐射与加速器束流动力学笔记, (Unpublished) 2024.
G. Stupakov, S. Heifets. Beam Instability and Microbunching Due to Coherent Synchrotron Radiation, Physical Review Special Topics-Accelerators and Beams, 2002, 5(5):054402.
K. L. Bane, Y. Cai, G. Stupakov. Threshold Studies of the Microwave Instability in Electron Storage Rings, Physical Review Special Topics-Accelerators and Beams, 2010, 13(10):104402.
金玉明, 电子储存环物理, 中国科学技术大学出版社，2001.
赵振堂，先进X射线光源加速器原理与关键技术，上海交通大学出版社，2020.
张耀，姜伯承，超瞬态装置储存环物理初步设计报告，2023.
F. Sannibale, J. M. Byrd, A. Loftsdottir, M. Venturini, A model describing stable coherent synchrotron radiation in storage rings, SLAC-PUB-10827, 2004.
J. Jarvis, et al., Experimental demonstration of optical stochastic cooling, Nature, Vol 608 2022.
D. Boussard. Cern/ps-bi[R]. Tech. rep., 1972.
Boris Podobedov and Robert Siemann, SIGNALS FROM MICROWAVE UNSTABLE BEAMS IN THE SLC DAMPING RINGS, Proceedings of the 1999 Particle Accelerator Conference, New York, 1999
A. Tremaine, J. Rosenzweig, and P. Schoessow, Electro magnetic wake fields and beam stability in slab-symmetric dielectric structures, Phys. Rev. E 56, 7204 (1997).
A. Blednykh , G. Bassi, and V. Smaluk, R. Lindberg, Impedance modeling and its application to the analysis of the collective effects, PHYSICAL REVIEW ACCELERATORS AND BEAMS 24, 104801 (2021)
Alexander Wu Chao, Lectures on Accelerator physics, World Scientific, 1st edition, 2020, ISBN 9789811227967.

## Slide 74
Thanks for listening!
jiangbocheng@cqu.edu.cn